## Slide 1: Ice Mining in Lunar Permanently Shadowed Regions
Chris Dreyer, George Sowers, Hunter Williams
Colorado School of Mines

## Slide 2: LCROSS Impactor 2009
LCROSS measured 5-10% water content by mass in Cabeus crater
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 3: Recap of Ice Value
Sell propellant from moon ice at 1100 mT/year, $0.5M/mT
Total non-recurring cost: $3.5B (Development + delivery)
Time for mine to become profitable: 5 years
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 4: The Case for Thermal Mining
Makes use of highest efficiency energy source, direct sunlight
With multiple mirrors in permanently lit region, maintains up to 99% sunlight through year
Lower mechanical complexity and tool wear than most concepts
Highly scalable
Background
Process
Concept
Control
Efficiency
Conclusion
Chart: 
| Efficiency
Solar | 0.9
Laser | 0.33
Microwave | 0.27

## Slide 5
Thermal Mining System Components
Direct solar
Heaters (optional)
Capture tent
Ice in cold trap
Electrolysis
Rocket fuel storage
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 6
Thermal Mining Process
Sublimation:
Rate controlled by heat
Boreholes with heaters
Heated zone
Tent:
Leak controlled by pressure
Cabling
Mobile cold trap:
Rate controlled by area
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 7
Thermal Mining Layout
Mirror system:
Gimbaled mirrors around peaks of eternal light
Base:
Electrolysis, storage, launch pad, etc
Thermal mining system:
Tent, optics, optional heaters
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 8
Thermal Mining Concept
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 9
Tent Pressure Control
Tent may rise as internal pressure rises, causing imperfect seal with ground and leak
Amount of gas leaked is small compared to amount trapped
Trapping rate in part governed by ratio of cold trap internal surface area to leak area
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 10
Ice Harvesting Rate Control
Background
Process
Concept
Control
Efficiency
Conclusion
Rather than design a heavy tent to stay grounded, use a lighter tent and minimize leaks with heat/pressure control
Leaked vapor will redeposit and enrich nearby area
Operating Temperature = 220K

## Slide 11
Possible Ice Types
Snow
(100% water)
Dirty ice
(90% by mass)
Icy regolith (4% by mass, hard packed, non saturated)
Background
Process
Concept
Control
Efficiency
Conclusion
Siegler et al 2012
Tepfers, R. 2008

## Slide 12
Thermal Mining by Ice Type
Chart: Temperature (K)
| 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240 | 250 | 260 | 270 | 280
 | 9.064e+55 | 1.8565e+43 | 5.9707e+34 | 4.8685e+28 | 1.2742e+24 | 3.3885e+20 | 4.5864e+17 | 2.0333e+15 | 2.1998e+13 | 473533816736.2059 | 17526086832.5075 | 1001803107.8799 | 81589436.8254 | 8900645.2099 | 1239511.1988 | 212127.3529 | 43273.106 | 10265.4135 | 2775.0508 | 840.657 | 281.4108 | 102.8777 | 40.6654 | 17.2326 | 7.7718
 | 9.1689e+56 | 1.8737e+44 | 6.0166e+35 | 4.9005e+29 | 1.2815e+25 | 3.4058e+21 | 4.6074e+18 | 20417694761918872 | 2.2082e+14 | 4.752e+12 | 175834513375.6779 | 10048643062.4036 | 818232604.4363 | 89246655.3301 | 12426725.4567 | 2126403.0871 | 433726.0557 | 102879.1648 | 27808.6427 | 8423.4362 | 2819.5261 | 1030.6815 | 407.3786 | 172.6225 | 77.8476
 | 9.1793e+57 | 1.8754e+45 | 6.0211e+36 | 4.9037e+30 | 1.2822e+26 | 3.4075e+22 | 4.6095e+19 | 2.0426e+17 | 2.209e+15 | 4.7537e+13 | 1.7589e+12 | 100517042607.6402 | 8184664280.5456 | 892706756.5317 | 124298868.0354 | 21269160.4291 | 4338255.5526 | 1029016.6775 | 278144.561 | 84251.2285 | 28200.6789 | 10308.7195 | 4074.5115 | 1726.5213 | 778.6047
 | 9.1804e+58 | 1.8755e+46 | 6.0216e+37 | 4.904e+31 | 1.2823e+27 | 3.4077e+23 | 4.6097e+20 | 2.0427e+18 | 22091008901996756 | 4.7539e+14 | 1.759e+13 | 1.0052e+12 | 81848981041.6386 | 8927307768.5482 | 1243020293.8223 | 212696733.8487 | 43383550.522 | 10290391.8042 | 2781503.7443 | 842529.1516 | 282012.2079 | 103089.0991 | 40745.8397 | 17265.5098 | 7786.1762
 | 9.1805e+59 | 1.8756e+47 | 6.0216e+38 | 4.904e+32 | 1.2823e+28 | 3.4077e+24 | 4.6097e+21 | 2.0427e+19 | 2.2091e+17 | 4753880186810720 | 1.759e+14 | 1.0052e+13 | 818492148652.568 | 89273317888.7129 | 12430234551.6919 | 2126972468.0448 | 433836500.2158 | 102904143.0715 | 27815095.577 | 8425308.3831 | 2820127.4972 | 1030892.8951 | 407459.122 | 172655.3947 | 77861.8914
 | 9.1805e+60 | 1.8756e+48 | 6.0216e+39 | 4.904e+33 | 1.2823e+29 | 3.4077e+25 | 4.6097e+22 | 2.0427e+20 | 2.2091e+18 | 47538818557593656 | 1758982453408000 | 1.0052e+14 | 8.1849e+12 | 892733419090.3601 | 124302377130.3879 | 21269729810.0059 | 4338365997.1544 | 1029041655.7446 | 278151013.9041 | 84253100.6977 | 28201280.3901 | 10308930.8558 | 4074591.9448 | 1726554.2429 | 778619.0434
 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400 | 158400
Choose optimal sublimation time for average ice particle size in ice field
Find temperature required to reach desired time
Heat surface to desired temperature using sunlight and heated boreholes
Background
Process
Concept
Control
Efficiency
Conclusion
Model adapted from Andreas, Edgar L. "New estimates for the sublimation rate for ice on the Moon." Icarus 186, no. 1 (2007): 24-30.
Age of Universe
Hours
Days
Millenia

## Slide 13
Mining Area by Ice Type
– Icy regolith (4% water) – Snow (100% water)
4 km
1 km2:
Area required for 10 years of icy regolith
0.05 km2:
Area required for 10 years of snow
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 14
Ice mined in 10 years at Shackleton
1 km2
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 15
Icy Regolith Capture Efficiency at 4%
Background
Process
Concept
Control
Efficiency
Conclusion
Requirement
Value
Area mined (m
2
/
year
)
100,000
Yield per
m
2
(kg)
16
Ice sublimated per
m
2
(kg)
18
Dwell time (
hour
)
44
Move time (
hour
)
12
Power (kW)
500
Tent
d
iameter
(m)
29
Tent
p
lan
area
(m
2
)
641
Exit area to cold traps
(m
2
)
2
Leak area
(m
2
)
0.2
Notes: Actual ice content is >60 kg per m2 in top meter of the surface assuming density of 1,500 kg/m^3 with 4wt% ice.

## Slide 16
Plant Efficiency
Background
Process
Concept
Control
Efficiency
Conclusion
Parameter | Excavation (for comparison) | Thermal Mining
Mass (kg) | 40400 | 29000 + optional heaters
Development cost ($) | 3.43B | 2.47B
Availability/ Maintainability | Medium | High

## Slide 17
Conclusion
Background
Process
Concept
Control
Efficiency
Conclusion
Thermal mining:
is an efficient, scalable, sustainable method of ice mining at the lunar poles
works in any ice type as long as there is pore space for vapor transport
benefits from direct solar energy transfer while using variable heating to control production rate
with lower weight and fewer moving parts, provides a feasible alternative to traditional excavation concepts

## Slide 18: Thank You!

## Slide 19: Mass Breakdown
Element | Excavation | Drilling | Passive | Max Drilling + Passive
Processing plant and storage | 6000 | 6000 | 6000 | 6000
Power & comms | 4100 | 4100 | 4100 | 4100
Mirror systems | 8400 | 8400 | 7500 | 4200+7500
Ice haulers | 2400 | 2400 | 2400 | 2400
General purpose vehicle | 1000 | 1000 | 1000 | 1000
2nd power plant | 4000 | 4000 | 0 | 2000
Excavation systems | 16500 | 6000 | 8000 | 3000+8000
Total | 40400 | 31900 | 29000 | 38200
Background
Process
Concept
Control
Efficiency
Conclusion

## Slide 20
Ice Capture Efficiency
Background
Process
Concept
Control
Efficiency
Conclusion
Requirement | Value
Area mined (m2 / year) | 100,000
Yield per m2 (kg) | 16
Ice sublimated per m2 (kg) | 18
Dwell time (hour) | 44
Move time (hour) | 12
Power (kW) | 500
Tent diameter (m) | 29
Tent plan area (m2) | 641
Exit area to cold traps (m2) | 2
Leak area (m2) | 0.2