## Slide 1: MOXIE Delivered!
Michael Hecht (for the MOXIE Team)
Space Resources Roundtabl3
June 2019

## Slide 2: The MEL for Mars
Plus: Propellant to leave Mars!
27 tons of O2
7 tons CH4

## Slide 3: Mars 2020

## Slide 4
M. Hecht, MIT/HO (PI)
J. Hoffman, MIT (DPI)
G. Sanders, JSC
D. Rapp, Consultant
B. Yildiz, MIT
G. Voecks, JPL
K. Lackner, ASU
J. Hartvigsen, Ceramatec
P. Smith, Space Expl. Instr.
W. T. Pike, Imperial Coll.
M. Madsen, U. Copen.
C. Graves, DTU (Coll.)
M. de la Torre Juarez, JPL (Coll.)
Jet Propulsion Laboratory
California Institute of Technology
J. Mellstrom , Project Manager
GOT OXYGEN?

## Slide 5: What will MOXIE do?
MOXIE is a 1:200 scale model of an ISRU plant for a human mission, ingesting CO2 from the atmosphere and producing propellant-grade O2
When running, MOXIE will make 6-10 g of oxygen per hour (about half as much as you need to breathe)
  6 g/hr is end-of-life design requirement
  12 g/hr is power supply limit.
  End-of-life is defined as 60 test cycles (10 cycles on Mars + 10 on Earth)x3
MOXIE will run for about an hour, approximately one day out of every 2 months (limited by rover power system).
O2 purity requirement is 98%. In practice, >99.6% consistently observed.

## Slide 6: How does it work?
Meyen (2015)
Notes: LSM – Lanthanum Strontium Manganate. CFY = Chromium Iron Yttrium

## Slide 7: Putting MOXIE together

## Slide 8: Final assembly

## Slide 9: State of the Project (JPL)
MOXIE has been delivered and is installed in the M2020 rover!
Life test in progress
“FlatSat” goes to MIT for further characterization
Primary mission from 2021-2023

## Slide 10: Operations
The Mars 2020 mission will launch in August 2020 and land in February 2021.
On Mars, MOXIE expects to operate for a ~2 hour session every 2 months (on average). Each operation will consume up to 1000 W-hr of spacecraft energy, corresponding to the full payload allocation for a typical day.
Three mission phases are planned:
  Characterizaation, when MOXIE subsystems will be checked out, the system will be commissioned, and performance will be increased incrementally from run to run until reaching maximum output;
  Operation, where MOXIE robustness will be assessed in a range of environmental conditions over much of the mission; and
  Exploration, where improved operational modes will be tested, limits of performance will be probed, and degradation under stress will be characterized.

## Slide 11: Limits to performance
The factors that limit performance are
  Power supply capability
  SOXE capability
  Compressor capacity
  Air density
    Landing site dependent
    Factor of 2 range from seasonal and diurnal variation
These factors are well-balanced in MOXIE, and it is unclear which will actually limit performance on Mars.

## Slide 12: Monitor and Control challenges
Measurement error is several percent on all sensors, including SOXE V, T.
  Behavior (stochastic? systematic?) not yet known.
  Uncertainty constrains operation to safe values well away from the Nernst threshold for coking (carbon formation).
Temperature gradients across the stack are >10ºC
  All cells should be 800ºC-830ºC for safe, effective operations
  Gradient and measurement uncertainty combine to constrain allowed T
Cells are wired in series. On flight model, V cannot be monitored cell-by-cell, eliminating ability to assess weakest cell (i.e. most prone to coking).
Redundant measurements for key parameters.
  O2 production given by I(SOXE), O2 sensor, CO sensor, or P(anode).

## Slide 13: SOXE Packaging
Several kN stack compression required to provide uniform contact between interconnects and electrodes
Together with the severe thermal insulation requirements, this drives the SOXE packaging architecture to a design that provides external spring compression through rigid insulating materials.
Ratio of (Stack Volume) / (SOXE Assembly Volume) is very small, but will get much better as scale of system grows.

## Slide 14: Dust filtering
Experiments and models show that the MOXIE filter is robust, even with respect to a hypothetical 10,000 hrs of operations
Dust mitigation is far less of a problem than expected because:
  Dust particles on Mars are ~10x larger than typically used for HEPA testing
  MOXIE operates in the transition flow regime, reducing ∆P by x3-5.
A tantalizing experimental result suggests that only ~4% of entrained dust actually impacts the filter if orthogonal to the airflow.
Intrinsic resistance of filtering material drives filter size & mass

## Slide 15: SOXE Degradation
Carbon deposition is avoidable by careful selection of operating voltages and temperatures
Cathode oxidation has been mitigated by recirculating CO to the inlet
Cycle-to-cycle (cool-heat) variation is significant but acceptable
  ASR roughly doubled after 60 cycles in first test; New test underway.
  Will get better as we learn about mechanisms and improve protocols
  Not really relevant to full-scale system, which won’t generally cycle
  Compensating by increasing cell area has little impact on overall M, V, P
Degradation from continuous long-term operation needs to be verified but expected to be low.

## Slide 16: Software architecture
Master Archive
Binary Translator
CSV
Translator
FlatSat
EM
Flight s/w (8150)
FSW emulator
(Labview)
Quick Viewer & Editor (Excel)
SS Model (Excel)
Error analyzer
Dynamic Model
SS Model
Matlab code
Other code
Hardware
Legend
STRUCTs (MAT Files):
RCTs & Parameter Tables
Metadata
Telemetry
Reduced data
CSV files
Binary files
Results:
STRUCT fields
CSV & MAT files
Plots
PDFs
FM
Command Builder
PDS Archive
XML
EDRs
RDRs
Dashboard
Data analysis
STRUCT fields for:
RCTs & Param Tables
Metadata
Commands
Data
Raw & reduced data:
STRUCT fields
Plots
PDFs
CSV files
Raw data:
Binary files
STRUCT fields
MAT files
XML
Translator
PDS Volumes
M2020 GDS
Pipeline Processor

## Slide 17: Testbed systems
JPL Testbeds are being decommissioned
MIT testbeds currently being outfitted
  FlatSat testbed at Haystack Observatory
  Sensor testbed in AeroAstro department
  Subsystem testbed TBD
  EM testbed will eventually be set up in AeroAstro

## Slide 18: Priority characterization activities
Acquire, organize, & evaluate JPL data
Understand magnitude and nature of measurement uncertainties
Validate table generation software and processes
Understand cell temperature behavior
  Steady state relationship of T(heater) and T(cells)
  Gradients across cells and dependence on current
  Time-dependent response to current step
Understand impact of "weakest cell" and implications for operation
Characterize compressor power profile
Extensibility studies (e.g. long-duration operation)

## Slide 19: Next generation
OxEon Energy is developing a scaled-up stack design with ~30x the capacity of a MOXIE stack.
  An array of 5-10 such units would producing >2 kg/hr O2.
  Other improvements reduce the tendency to coke or oxidize.
  New designs to reduce the need for compression would be advantageous.
Air Squared is working on a scaled up version of a compressor
  For MOXIE, the compressor is a large fraction of the mass and power budget
  This could be reduced by operating at lower pressure, ~100 mbar.
Filters consume a disproportionate amount of mass and volume.
  Identifying lower resistance material should be a high priority.
  Additional research is needed on dust entrainment and capture

## Slide 20: Sponsors and Partners
Supported by HEO/AES, STMD/Tech Demos
Mars 2020 Project managed by SMD
ISRU Technology, NASA GRC
Aarhus wind tunnel
Thank you,
Congrats & Thanks, Forrest!

## Slide 21: Backup
More MOXIE

## Slide 22: MOXIE Data Products
Raw data: EDRs
  Raw sensor readings
  Values calculated in situ
  Event records
  Ancillary information to support thermal and performance models
  Diagnostics
Partially Processed (RDR):
  Data products in physical units based on nominal calibrations
Calibrated (RDR):
  Data products in physical units based on latest calibration, derived in part from the present data set.
Derived: Time series of calculated quantities
  Inlet flow rate
  O2 production rate
  O2 purity
  CO2 utilization efficiency
  Open circuit voltage
  Area Specific Resistance
  Filter resistance
  Compressor efficiency
Derived: Higher order Products
  Electrochemical potentials
  Dust accumulation rates
Others TBD

## Slide 23
Theme Groups
Environments and Dust
ISRU & Extensibility
SOXE Technology
Flight
s/w
Software Development
Data analysis & modeling s/w
Uplink s/w
MOXIE Testbeds
DP Testbed
EM Testbed
SOXE & assembly
Engineering support
Mechanical & Thermal
Electronics & S/W
Education & Outreach
Publications & presentations
Knowledge Products
Legacy Documentation
PI &
DPI
M2020 PSG
Operations
Technology
Science
PUDL | Payload uplink/downlink lead
SCL | Strategic & campaign lead
DPO | Development Prototype Operator
EMO | Engineering Model Operator
SDTE | Software development & test engineer
DAA | Data analyst and archivist
LM | Lab manager
MOCL | MOXIE Operations Center Lead
Doc | Documentarian
TEL | Technical Engineering Lead
PI | Principal Investigator
DPI | Deputy Principal Investigator
CoI | Co-Investigator
TGL | Theme Group Lead
COL | Collaborator
SPD | Student / Postdoc
AST | Associated staff
Admin | Administrative support
Science roles
Operations roles
Uplink/Downlink PUDL
Data analysis & archival
MOXIE Operation Centers
Strategic & Campaign Planning
Tactical implementation
RCT development & validation
Admin Support

## Slide 24: MOXIE Table types
Run Control Tables (RCT)
  Master control for a MOXIE run
  All parameters that can be changed step-wise
    ISOXE, Tsoxe, P4, etc.
Parameter tables
  Three types:
    Safety limits
    Algorithm parameters
    Run parameters
  Not changable step-wise!
  Critical that we maintain association with RCTs!
Metadata (Science Team use only)
  Information used for simulations
    SOXE ASR, external P/T, etc.
    Parameter table IDs
    Command sequence IDs
    Archival data IDs
  We should also create these to accompany archival flight data

## Slide 25: Run Control Table content
# of Steps | Up to 64
Step # | (0-63)
Duration | Seconds
TSOXE setpoints (2) | SOXE Temperatures, Top and bottom
TSOXE limits (4) | Max, min limits, Top & Bottom (abort if exceeded)
P4 setpoint | Controls compressor speed.
P4 offset | Allows fixed compressor speed to be set
P4 limits (2) | Max, min limits (abort if exceeded)
ISOXE setpoints | SOXE current(s), Top & Bottom
ISOXE offset | Allows fixed voltage to be set
Utilization limits (4) | Max, min limits, ISOXE/P4: Top & Bottom (abort if exceeded)
Enable flags (6) | SOXE heaters; CO2 & CO sensors; O2 sensor; Compressor; VSOXE (2)

## Slide 26: Parameter Table content
Algorithm parameters | 
Persistence on/off | Logical flag indicating if persistence is specified
Proportional Gain (5) | TSOXE (2), P4 (compressor), ISOXE (2)
Integral Gain (5) | TSOXE (2), P4 (compressor), ISOXE (2)
Limiter, minimum (3) | P4 (compressor), ISOXE (2)
Limiter, maximum (7) | P4 (compressor), TSOXE w/ V enabled (2), TSOXE w/ V disabled (2) , ISOXE (2)
Persistence (5) | TSOXE (2), P4 (compressor), Utilization ISOXE/P4 (2)
Safety Limits | 
Persistence on/off | Logical flag indicating if persistence is specified
Pressure (4) | Max pressure in P2,3 (flow), P4 (cathode exhaust), P5 (anode exhaust)
VSOXE (2) | Max SOXE Voltage
V28V supply (4) | Max and min for Main & SOXE 28V supplies
ISOXE (2) | Max SOXE Current
TSOXE (2) | Max SOXE Temperature
Temperature (6) | Max T1 (sensors), T3,4 (compressor), T22 (power board); T7 max, min(baseplate)
Persistence (17) | P2,3,4,5, VSOXE (2), V28V (2), ISOXE (2), TSOXE (2), T1,3,4,7,22
Run parameters | 
Persistence on/off | Logical flag indicating if persistence is specified
CO2+CO current limit | Combined maximum for SmartGas sensors
O2 current limit | Maximum for Pyroscience sensor
Persistence (2) | For two items above