## Slide 1: Conceptual Design of ISRU Propellant Storage Depots
Colorado School of Mines
Graduate Research Assistant:
Lee Johnson
Advisors:
Dr. Robert King & Dr. Michael Duke, CSM
Extraterrestrial ISRU Systems Concepts Development
Mr. Kerry Nock, Global Aerospace Corporation

## Slide 2: This Presentation Will Cover The Following Topics:
Overview of the GAC Astrotel Project
System (Design & Assumptions) Requirements
Overall System Design
  Lunar Surface Depot Flow Block Diagram
System Design (Using Lunar Depot Model)
  Storage Tanks (Cryogenic, Gaseous)
  Electrolysis/Dryers/Radiators
  Liquefiers/Radiators
  Solar Arrays (Total Power Consumption)
Conceptual Drawings of Other Depot Facilities
Conclusions and Recommendations

## Slide 3: The GAC Astrotel Architecture Provides Cyclical Transport To Mars.
The Astrotel Project Provides:
  Transport between Earth & Mars via small, highly autonomous vehicles called Astronaut Hotels.
  Frequent & short duration trips between the two planets (5 month duration).
The Astrotel Architecture Requires:
  In-situ resource excavation, processing & storage.

## Slide 4: The Conceptual Designs Are Based On The System Requirements & Technology Assumptions.
System Requirements
  Production, Delivery or Storage Rates:
    Liquid Water
    Oxygen/Hydrogen Gas
    Liquid Oxygen/Hydrogen
    Electrolysis
    Liquefaction
Technology Base (Assumptions)
  Component Specs:
    Solar Arrays
    Electrolyzer
    Dryers
    Liquefiers
    Radiators
    Storage Tanks
  System Effects:
    Component Volume, Size, & Mass
    Power Consumption

## Slide 5: The Conceptual System Design Is Broken Down Into Five Sections.
Storage Tanks
Electrolysis
Dryers & Radiators
Liquefiers & Radiators
Solar Cells (Total Power Consumption)

## Slide 6: All System Components Are Based On Data Obtained From The Following References.
“Conceptual Study of On Orbit Production of Cryogenic Propellants by Water Electrolysis”. Moran, M.E. NASA Lewis Research Center. 1991. NAS1.15:203730
“Cryogenic Reactant Storage for Lunar Base Regenerative Fuel Cells”. Kohout, L.L. NASA Lewis Research Center. 1989. NAS1.15:101980
“Cyclical Visits to Mars via Astronaut Hotels: Phase I Final Report”. Global Aerospace Corporation. 30 November 2000. GAC Report #:510-04911-007

## Slide 7: Lunar Surface Propellant Depot
Depot Requirements:
  Store 10,056 kg water
  Convert water to oxygen & hydrogen @ 4.5 kg/hr
  Liquefy Oxygen @ 3.94 kg/hr
  Liquefy Hydrogen @ 0.56 kg/hr
  Daily transfer of LOX & LH to L1 depot, tanks sized for daily storage.

## Slide 8: Lunar Surface Depot System Flow Block Diagram

## Slide 9: The Tanks Store the Necessary Amounts of LOX, LH, and Water.
Water Storage
  For Liquid Water:
    Nominal Density=980kg/m3
    Conversion:
    1.02 m3/M.T.
    Required 10.056 M.T. water storage gives: 10.3 m3 volume.
    Volume rounded to 10.5 m3 for insulation & other items.
Cryogenic Storage
  Assumed aluminum dual layer construction w/insulation.
  Tank size includes an additional 15% for residual & maximum achievable filling level.
  For LOX: 0.947 m3/M.T. with the required 0.032 M.T. gives 0.03 m3.
  For LH: 15.6 m3/M.T. with the required 0.005 M.T. gives 0.07 m3.

## Slide 10: The Electrolysis Unit Separates The Water Into Oxygen & Hydrogen.
Assumed electrolyzer specifications:
  Alkaline medium, 355 K operating temperature, 2.17 MPa operating pressure.
  4.41 kWh/kg h20 Electrolyzed
  12.26 kg equip/kW Required
  7.88*10-4 m3 Volume/kg equip (Includes dryers)
  87.6% Electrolysis output oxygen gas & water vapor
  12.4% Electrolysis output hydrogen gas & water vapor
Applying this to the Lunar depot:
  Volume=0.19 m3 & Required Power=19.3 kW

## Slide 11: The Dryers Take Out The Water Vapor From The O2 & H2 Gases.
Assumed dryer specifications:
  2 step drying system: cold trap condensation and absorption/adsorption with hydroscopic salt.
  Output 98.9% pure oxygen gas from input gas/water vapor mixture.
  Output 86.9% pure hydrogen gas from input gas/water vapor mixture.
  Dryer Radiator Sizing:
    1.81 kg equip/kg/hr input mixture
    0.17 m2/kg equipment
Applying this to the Lunar depot:
  Oxygen Dryer Radiator Surface Area=1.2 m2
  Hydrogen Dryer Radiator Surface Area=0.17 m2

## Slide 12: The Oxygen & Hydrogen Liquefiers Refrigerate The Gases To A Liquid State.
Assumed liquefier specifications:
  Liquefiers both cool the incoming gas from the dryers and the boil-off gases from the storage tanks.
  Hydrogen Liquefier:
    24% Carnot Efficiency, 16.4kWh/kg H(l), 0.2705 kWh cool/kg H2(g), 0.7kg equip/W cool, 0.0012 m3/kg.
  Oxygen Liquefier:
    20% Carnot Efficiency, 0.9kWh/kg H(l), 0.0707 kWh cool/kg H2(g), 0.1kg equip/W cool, 0.00306 m3/kg.
  Liquefier Radiators:
    T reject @ 340 K. 26.3 kW reject/kg/hr hydrogen produced, 1.2 kW reject/kg/hr oxygen produced, 10 kg equip/kW reject, & 0.14 m2/kg equip.
Applying this to the Lunar Depot:
  Oxygen: V=0.08 m3, Required Power=3.6 kW, Radiator SA=6.5 m2
  Hydrogen: V=0.1 m2, Required Power=9.2 kW, Radiator SA=6.5 m2

## Slide 13: The Solar Arrays Are Sized For The Total System Power Requirements.
Assumed solar array specifications:
  Flat solar arrays with ~14% efficiency.
  2400 W/kg equip, .08 kg equip/m2
  Additional 7% of total power requirement added for power conversion & distribution (93% efficiency)
  Additional 8% of total power requirement added for misc. equipment.
Applying this to the Lunar Depot:
  Total Power Required (Including misc. equipment)=36.8 kW
  Flat Solar Array Surface Area=192 m2

## Slide 14: Using These Component Calculations, Conceptual Drawings Were Drawn For The Other Three Facilities.
Calculations applied to the specific requirements of the GAC Astrotel project.
Four conceptual depots:
  L1 Spaceport
  Lunar Surface
  Mars Surface
  Mars/Phobos Orbit

## Slide 15: L1 Spaceport Propellant Depot
Depot Requirements:
  Store 3,818 kg water
  Convert water to oxygen & hydrogen @ 1.59 kg/hr
  Liquefy Oxygen @ 1.42 kg/hr
  Liquefy Hydrogen @ 0.18 kg/hr
  LH Storage 387 kg
  LOX Storage 3099 kg

## Slide 16: Lunar Surface Propellant Depot
Depot Requirements:
  Store 10,056 kg water
  Convert water to oxygen & hydrogen @ 4.5 kg/hr
  Liquefy Oxygen @ 3.94 kg/hr
  Liquefy Hydrogen @ 0.56 kg/hr
  Daily transfer of LOX & LH to L1 depot, tanks sized for daily storage.

## Slide 17: Mars Surface Propellant Depot
Depot Requirements:
  Store 1,147 kg water
  Convert water to oxygen @ hydrogen @ 8.07 kg/hr
  Liquefy Oxygen @ 7.06 kg/hr
  Liquefy Hydrogen @ 1.01 kg/hr
  LOX Storage 3,824 kg
  LH Storage 30,593 kg

## Slide 18: Mars/Phobos Orbit Propellant Depot
Depot Requirements:
  Store Oxygen Gas 189 kg
  Liquefy Oxygen 23.2 kg/hr
  LOX Storage 17,272 kg
  LH Storage 2,467 kg
  Assume LH from earth.

## Slide 19: Conclusions & Recommendations
Technology & calculation assumptions suited for a conservative initial system conceptual design.
Improvements in equipment selection from trade studies of more recent space-specific applications.
Improvement in component mass/size assumptions would include associated equipment such as mounting structures, pumps, etc.