## Slide 1: Development of a Surface Exploration Infrastructure Based on Common Technologies & ISRU Consumables
Jerry Sanders
Chief, Propulsion & Fluid Systems Branch
Energy Systems Division/JSC/EP4
(281) 483-9066
gerald.b.sanders@nasa.gov
Oct. 28, 2003

## Slide 2: NASA Vision & Mission & Exploration Overview
NASA’s Vision is to “ …improve life here, extend life to there, and find life beyond”
NASA’s Mission is to “…understand and protect our home planet, explore the Universe and search for life, and inspire the next generation of explorers … as only NASA can”
Exploration Overview:
  Missions are science-driven and not destination-driven
  Progressive expansion of robotic and human exploration from Earth Orbit to:
    Earth’s Neighborhood (Moon & Earth-Moon Lagrange Points)
    Sun-Earth Lagrange Points
    Assessable & Sustainable Planetary Surface Exploration
    Outer Planets
    Beyond
To Meet NASA’s Mission and to meet the challenge “to explore the universe and search for life” robotic and human exploration must be Affordable, Beneficial, and Safe

## Slide 3: Attributes of an Exploration Infrastructure that Utilizes Common Technologies and ISRU Consumables
Robotic, Beyond Planets
R8
Affordable
  Maximizes use of common hardware in multiple applications and at multiple destinations of interest (mission not destination driven)
    Reduces development and recurring costs
    Enables modularity that can reduce logistics of spare parts (ex. EVA fuel cell uses one FC module, EVA robotic rover uses 3 FC modules, and human rover uses 10 FC modules)
  Minimizes Earth launch mass & costs
  Maximizes reusability
Beneficial
  Enhances or enables new missions and science by:
    Extend mission durations beyond Earth-supplied consumables
    Increasing surface mobility and number of sites of exploration
    Increasing delivered payload for same size Earth launch vehicle or lander
Safe
  Provides functional backup to life support system and can increase radiation protection
  Reduces dependence on Earth supplied products (especially for long trip times)
  Increases options in event of problems or failures
    Modular hardware enables scavenging of replacements for failed hardware in emergency
    Common consumables enables crew to scavenge oxygen and fuel from rovers to extend mission or overcome power or life support failures

## Slide 4: Surface Exploration Based On ISRU
Human/Robotic missions to the surface of the Moon and Mars will require:
  Tele-robotic rovers and aerial vehicles for science, site reconnaissance, and potentially hazardous operations.
  Autonomous and tele-robotic rovers for planetary resource excavation, transport, and processing
  Power-rich Extra-Vehicular Activity (EVA) suits for lights, tools, computers, communication, etc.
  EVA assistant rovers for site exploration
  Human transport rovers and propulsive hoppers for mid and long distance exploration
  Emergency cache of critical life support consumables for habitat and spacecraft
  Consumable cache for EVA operations
  Enhanced radiation protection (long-duration)
ISRU can provide the following mission critical consumables & materials:
  Propellants for propulsion systems:
    Oxygen (O2)/Fuel for landers, hoppers, and aerial vehicles
    Water & O2/hydrogen (H2) for cargo transportation vehicles and space stations
  Reagents for fuel cell power systems
  Life support consumables (O2, N2, water) for habitats, airlocks, and EVAs
  Gases for science equipment (N2, Ar, H2, He, etc.) and drilling
  Extra radiation shielding from regolith or in-situ water resources

## Slide 5: Surface Exploration Infrastructure Concept
Robotic Precursors & Tele-robotic Science
EVA Astronaut w/ Robotic Assistant
EVA Astronauts w/ Pressurized or Un-Pressurized Rovers
Short trips from habitat
8 to 10 hrs
Lots of start/stops for science
Resupply EVA O2 & FC reactants from Rover to extend EVA or emergency
Long trips from habitat
1 to 5 days
EVA’s only for pre-screened science
Rover stores EVA O2 and power consumables – recharged before each EVA
Short trips from habitat or lander
Lots of start/stops for science
Lander or habitat resupplies Fuel Cell (FC) reactants when rover returns with samples
Short trips (4 to 10 hrs)
Rover carries equipment & supplies power
Resupply EVA O2 & FC reactants from Rover to extend EVA or emergency
Modular hardware & common consumables for reduced logistics, and increase flexibility, & safety
ISRU plant on Lander or Habitat produces consumables for EVA and rover life support & power initially
Infrastructure is easily expandable from simple robotic lander and rover to full human presence
Landers
ISRU plant on Habitat Lander
  Propellant tanks used for FC reactant & ELCSS backup storage
Crew Lander reused with ISRU Propellant

## Slide 6: Common Technologies Enable Multiple Applications
Surface Infrastructure
Subsystems
Core Technologies
Robotic Precursors & Tele-robotic Science
EVA Astronaut w/ Robotic Assistant
EVA Astronauts w/ Pressurized or Un-Pressurized Rovers
Habitats
Landers
Fuel Cell Power
Open-Loop Life Support
Closed-Loop Life Support
Consumable Production
O2-Based Propulsion
In-Situ Production Of Consumables
CO2 & N2 Acquisition & Separation
Sabatier Reactor
RWGS Reactor
CO2 Electrolysis
Methane Reforming
H2O Separators
H2O Electrolysis
H2O Storage
Heat Exchangers
Liquid Vaporizers
O2 & Fuel Storage (0-g & reduced-g)
O2 Feed & Transfer Lines
O2/Fuel Couplings
Fuel Cells
O2/Fuel Igniters & Thrusters

## Slide 7: Development of Surface Infrastructure Concept
Need
  Demonstrate feasibility of Surface Exploration Infrastructure concept
    Develop mobile power system capable of delivering high peak power and high total energy for long duration operations over a wide range of environmental conditions
    Demonstrate capability in simulated mission operations
    Demonstrate “power rich” environment for science
  Develop experience with near-term technologies to assess interoperability with power, propulsion, and life support systems and direct future technology development activities
  Develop and demonstrate prototypes of design that can be used as basis for future partnerships or NRA solicitations
Approach
  Select initial applications with modest mass, volume, and integration limitations
  Develop evolvable testbed for technology and operations development and demonstration
  Build-a-little, test-a-lot
  Evolve technologies and surface infrastructure assets with experience
  Initiate project to:
    Support development of Robotic/Human Interaction
    Leverage existing-but-separate JSC activities into a common program
    Provide young engineers with hands-on experience in systems and operations

## Slide 8: ISRU Hydrogen/Oxygen Power Plant (IHOPP)
Objective
  Demonstrate and characterize the feasibility of powering an EVA Assistant Rover with a fuel cell (FC) using ISRU-producible reactants
  Requirement
  Replace existing battery power system with more capable FC system
    Fuel Cells & 3 High Pressure Tanks (1 O2, 2 H2)
    Power: 1200 W @ 24 V, 1600 W @20 V
    Power Density: 8.76 kW*hr; 139W*hr/kg
    Duration: 13.5 hours @ 600 W ave. power
    Envelope: 38” L, 30” W, 24”) H (approx.)
    Mass (wet): 63 kg (139 lbm)
  Plan
  Develop & demonstrate mobile fuel cell power system in 3 Phases
    Phase 1: ISRU Hydrogen/Oxygen Power Plant (IHOPP) FY02
    Phase 2: ISRU Methane/Oxygen Power Plant (IMOPP) FY03
    Phase 3: ISRU Cryogenic Methane/Oxygen Power Plant (ICMOPP) FY04
  Results
  Successfully tested at Meteor Crater, Arizona in Sept. 2002
IHOPP
2nd Gen EVA Rover
1st Gen EVA Rover

## Slide 9: Science, Crew, Operations & Utility Testbed (SCOUT)
  Objectives
  Select initial applications with modest mass, volume, and integration limitations
  Develop evolvable testbed for technology and operations development and demonstration
  Evolve technologies and surface infrastructure assets with experience
  Requirements/Goals
  Accommodating 2 person suited crew (600 lbm total)
  Easy ingress/egress of crew and payload
  Support manual, teleoperation, and autonomous control & operations
  Transport over rough terrain and long distances
    >10o slope (30o Mars equivalent), 1 ft tall rocks
    Minimum 6 mile round trip, goal 60 miles max
  Minimum 6 mile round trip (FY05 goal 60 miles)
  Carry and/or tow payload
    Carrying up to 400 lbm (in addition to crew)
    Towing payload trailer of up to 500 lbm
  8 KW PEM fuel cell power plant
  Provide power and consumables for crew and science support
    Provide power and/or consumables to crew while in transit
    Provide power to science equipment while in transit (TBD W) and at rest (TBD W)
  Provide non-line of sight communication and navigation from base

## Slide 10: SCOUT (Cont.)
  Plan: Yearly Integrated Tests and Field Test articles:
    FY03: Subsystem & Ops Test Unit:
      Modify Apollo Lunar Rover with PEM fuel cell power plant (H2, O2 gaseous storage)
      Initiate fuel reformer, cryogenic storage and navigation system designs
      Human Factors Testbed (HFT)
      Testbed for automation, communications, sensors, and control systems
    FY04: SCOUT Engineering Unit (EU):
      Demonstrate 1st iteration on motion system and crew/payload accommodations
      Incorporate and demonstrate additional subsystems not demonstrated in first year
    FY05: 1st Gen SCOUT Unit tested at year’s end field trials
  Results
  Successfully tested at Meteor Crater, Arizona in Sept. 2003
  Power plant operated successfully but needs to be more durable
  Operating environment much more severe than at JSC “Mars yard”
  Lots of lessons learned (hardware & operations) to be used in 1st SCOUT unit

## Slide 11: Potential Interoperability & Evolution of Surface Infrastructure Technologies & Capabilities
EVA Assistant Rover
EVA Suit Power
SCOUT Rover
Gaseous H2/O2
Gas CH4/ Liquid O2
Liquid CH4/O2
Gaseous H2/Liquid Air
1st Demonstration in Arizona Sept., ‘02
Liquid CH4/O2
Liquid CH4/O2
Liquid O2
Lunar Polar Explorer
Long-Range Rover
Power Rich EVA
Gaseous H2 / Liquid O2
1st Demonstration in Arizona Sept., ‘03
Gaseous H2/O2
Robotic Colonies
Liquid O2 or Air, Gas H2
Gas CH4/ Liquid O2
Hybrid Battery – FC Gaseous H2/O2