## Slide 1: Lunar Materials Handling System
Pioneer Astronautics
Lakewood, Colorado
Mark Berggren, Robert Zubrin, Stacy Carrera, James Kilgore, John Campbell,
Heather Rose, Nick Jameson,
Curt Boyll, Christine Roark
NASA JSC SBIR Phase I
Contract NNJ06JD81C;
Landon Moore, COTR
Space Resources Roundtable VIII
November 1, 2006

## Slide 2: ISRU Background and Problem
Many lunar ISRU processes have been demonstrated on a laboratory scale.
For repeatable, long-duration operations, a lunar ISRU system will need to address the following critical issues :
  Gas leaks from process seals
  Component damage by abrasion or heat
To capitalize on ISRU, materials handling and reactor systems that address these issues are required.

## Slide 3: LMHS Description
The Lunar Materials Handling System (LMHS) conveys solids to and from an ISRU process vessel and provides a gas-tight seal
  Protects seals from abrasive wear
  Protects internal reactor components from radiant process heat
  Protects external components from environmental temperature extremes
LMHS methods enable automated feeding, equipment operation, and residue discharging over many cycles.

## Slide 4: LMHS Phase I System

## Slide 5: LMHS Phase I Work Plan
Select candidate valve and seal types.
Characterize valve and seal durability.
Characterize particle flow and adhesion using JSC-1 simulant.
Develop seal contaminant protection methods.
Develop seal cleaning methods.
Demonstrate LMHS techniques integrated with ISRU processing in vacuum.

## Slide 6: LMHS Phase I Valve Selection
Ball valves, gate valves, and custom hatches with elastomer seals were identified for LMHS applications.
  Each has a wide, clear flow path
  They can withstand or be protected from environmental and process temperature extremes
  Some elastomer seals are capable of operating over many compression-decompression cycles at temperatures from –260 to +320°C.

## Slide 7: LMHS Phase I Valve Selection
Ball Valve
  Rotating seals (Teflon®)
  Higher profile
  Resistant to abrasive wear over dozens of cycles

## Slide 8: LMHS Phase I Valve Selection
Gate Valve
  Perpendicular seal engagement
  Lower profile
  Sensitive to particulate contamination

## Slide 9: LMHS Phase I Characterization
Particle Adhesion
  Polished surfaces reduce adhesion and aid flow
  Layer of ultra-fine particles adhere regardless of material, finish, or electrical charge
Gore-Tex®
Polished Stainless Steel
Particle Flow & Adhesion Experiments

## Slide 10: LMHS Phase I Characterization
Surface Cleaning
  Electrostatic, magnetic, and vibration methods remove most particles.
  Wiping is effective, but abrades surfaces
  Pneumatic pulses provide effective, non-contact cleaning
Electrostatic “Fountaining”
Pneumatic Pulse Experiments

## Slide 11: LMHS Phase I System Design
Seal Protection
  Contaminant prevention is the preferred method to ensure long-term seal reliability
  Seal cleaning provides secondary protection
  System designed using a ball valve; design is readily adaptable to gate valves or hatches
Integrated Feeder and Valve Protection Sleeve

## Slide 12: LMHS Phase I Demonstration
System Demonstration
  Automated LMHS operated in 1 m3 vacuum chamber
  LMHS integrated with hydrogen reduction
    Batch, down-flow reactor
    Sealed H2 system
    H2 recycle pump
    H2O recovery
  Multiple operations (~850°C; 5 hr cycle time)
LMHS in
Vacuum Chamber
H2 Reduction,
Vac Chamber,
Controls

## Slide 13: LMHS Phase I Demonstration

## Slide 14: LMHS Phase I Demonstration
Demonstration Results
  No H2 leaks
  2 % O2 yield from JSC-1
  Successful material feed and discharge from reactor
  No valve contamination or wear
Process Ball Valve
After Operations
Alumina Felt Seals
Wiper
Dust Contained
in Sleeve
Discharge Valve Protection Sleeve

## Slide 15: Future Work
Build and test a 1 kg per day O2 LMHS/hydrogen reduction system
Demonstrate repeated operations in vacuum
Establish net yield, operating power, heat exchange requirements, and hydrogen losses
Apply knowledge to establish LMHS needs for alternate ISRU processes
Evaluate LMHS commercial applications

## Slide 16: Acknowledgements
NASA Johnson Space Center
SBIR Program
Landon Moore (JSC)