## Slide 1: A Long-Endurance Retaskable Transfer Vehicle
Brad R. Blair
Justin G. Rodriguez
Gary J. Rodriguez
presented at the 8th Annual Space Resources Roundtable, Golden, Colorado
November 1, 2006
sysRAND Corporation
Space Commercialization and Development
Propellant Supply Issues

## Slide 2: Overview
Expendable vehicle analogy
Currently reusable launch elements
Propellant supply options
Near term applications

## Slide 3: An expendable vehicle analogy Did Henry Ford enable Standard Oil to prosper?

## Slide 4: The ‘Expendable Honda’ model (an analogy for how we currently conduct space transportation)
Model Assumptions
  New car must be purchased when fuel tank is empty
  Standard driving conditions = 12,000 miles per year
  Standard options, Minimum vehicle price
  Fuel tank capacity + MPG used in analysis
  Assume highway mileage applies through life of vehicle
2006 Ridgeline $27,700 MSRP
Fuel Tank Capacity: 22.0 (gal.)
EPA Mileage Estimates:
16 mpg / 21 mpg (Cty/Hwy)
Payload Capacity: 1,550-lb.
2005 Civic $13,675 MSRP
Fuel Tank Capacity: 13.2 gal.
EPA Mileage Estimates:
32 mpg / 38 mpg (Cty/Hwy)
Payload Capacity: 13 cubic ft
2005 Insight $19,845 MSRP
Fuel Tank Capacity: 10.6 gal.
EPA Mileage Estimates:
60 mpg / 66 mpg (Cty/Hwy)
Payload Capacity: 16 cubic ft

## Slide 5: EH Model – Annual Results
Annual capital cost of driving: $330,000-$720,000
Not included: Operations, maintenance, fuel cost
Question: How would this change automobile demand?
Rocket Stages are Discarded after their first use!

## Slide 6: Extending EH range to >500mi Systems Requirements for a single cross-country road trip (remember - no filling stations)
Load onto expendable flatbed 1000mi $50,000
Load flatbed onto tractor-trailer 2000mi $250,000
Load tractor-trailer onto train 3500mi $1,250,000
Load passenger into EH 500mi $15,000
Action Range Cost
A linear increase in distance incurs an exponential cost!

## Slide 7: Reusable launch elements exist in today’s launch fleet (upgrades will be required…)

## Slide 8: An outside look at the current space launch fleet
Delta 4H
Atlas V Heavy
Ariane 5G
Delta II
Soyuz
Proton
Zenit 3SL
Atlas
V400
Atlas IIAS
Delta 4M
H-IIA
GSLV
CZ-3A
Atlas V552
Saturn V
Saturn I
Atlas LV3B
Redstone
Titan-II
Shuttle
Titan IVB
Apollo
Era
retired
Shuttle
Era
nearly retired
Current US
Launch Fleet
International
Launch Fleet

## Slide 9: Potentially reusable elements in today’s launch fleet (LOX / LH2 cryo stages)
Shuttle ISS
2040 tons
$300M(2002)
Ariane 5G
746 tons
$165M(2002)
Atlas V 400
333 tons
$90M(2002)
Atlas IIAS
234 tons
$97.5M(2002)
Delta 4M
256 tons
$95M(2002)
H-IIA
289 tons
$80M(1999)
GSLV
402 tons
$45M(1999)
Titan IVB
886 tons
$400M(1999)
CZ-3
241 tons
$55M(1999)
Ariane 44L
475 tons
$120M(2000)
Delta 4H
726 tons
$187M(2002)

## Slide 10: Four elements will be examined in detail
Shuttle External tank
Boeing Delta IV
Upper stage & Core booster
Lockheed-Martin Atlas II
Centaur upper stage

## Slide 11: The Centaur Upper Stage
Currently discarded when empty!
Atlas Centaur II-A upper stage
Gross mass
  19,100kg
Empty mass
  2,300kg
Propellant mass
  16,800kg
ISP
  449 sec
Standard payload to LEO
  8,600kg (Atlas IIAS, standard config)

## Slide 12: Centaur Reuse
Approximate payload of a fully fueled Centaur IIA in LEO
  To GEO – 7,700kg
  To LLO – 8,900kg
Centaur upper stages are currently classified as “orbital debris”
Number of Centaurs remaining in orbit > 90 (out of more than 170 launches)
Location
Conclusion
  Transportation infrastructure is already accumulating in Earth orbit
  These could be stranded assets

## Slide 13: Boeing Delta IV-Heavy
Largest vehicle in the international launch fleet
  All components utilize LOX/LH2 cryogenic propellants
  The HDCUS upper stage is potentially reusable
  The central core stage can be put into LEO, and is also a candidate for reuse
The potential LLO payload of a LEO refueled Delta-IV core booster is more than 3x the LLO payload of the Saturn V

## Slide 14: Boeing Delta IV-Heavy: Upper Stage
Technical Specifications
  Gross Mass – 30,200kg
  Empty Mass – 3,500kg
  Propellant Mass – 27,000kg
  ISP – 462 sec
Delta IV Standard Payload
  LEO – 25,800kg
  GTO – 10,800kg
  LLO – 6,700kg (est)
Refueled in LEO: Extended Payload
  GEO – 13,200kg
  LLO – 15,000kg
  L1 – 17,000kg

## Slide 15: Boeing Delta IV-Heavy: Core Booster
Technical Specifications
  Gross Mass – 226,400kg
  Empty Mass – 26,800kg
  Propellant Mass – 199,600kg
  ISP – 420 sec
Delta IV Standard Payload
  LEO – 25,800kg
  GTO – 10,800kg
  LLO – 6,700kg (est)
Refueled in LEO: Extended Payload
  GEO – 80,600kg
  LLO – 93,100kg
  L1 – 106,600kg

## Slide 16: Utility of the Shuttle External Tank
Shuttle ET statistics
  720 tons fuel capacity
  30 tons dry mass
  No engines
  Insulated
  Can be directly inserted into LEO 28.5o orbit
Propellant depot utility
  Largest off-the-shelf tank transported to LEO
  Designed for short-term storage of LOX & LH2
  Early utilization could store propellants as a pressurized gas
System upgrades
  Long-term storage
  Add MMOD shielding + MLI, cryocoolers, power, electrolysis, fluid handling & sensors
  Could be launched as a separate payload package
Reuse of the Shuttle ET for propellant storage could provide significant savings to fuel depot operator

## Slide 17: Recap: Extending the ‘reach’ of existing launch assets
Atlas II
140 tons LEO
27.5 tons LLO
14.5 tons Moon
Delta IV-H
Primary Assumption
LV stages are configured for reuse (not realistic for current fleet elements - actual performance will be somewhat reduced)
Conclusions
HLLVs may not be necessary for a human lunar return
Detailed engineering for a refueling depot in LEO is justified
Expected performance increase supports the business case
In-depth propellant market & depot cost analysis is justified
Apollo Baseline
Standard
25.8 tons LEO
Standard
8.6 tons LEO
Standard
25.8 tons LEO
Refueled upper stage
15.0 tons LLO
Refueled
Centaur IIA
8.9 tons LLO
Refueled core booster
93.1 tons LLO

## Slide 18: Supplying propellant to LEO

## Slide 19: Propellant Depot Trade Space
Supply Options
  Launch propellant directly from Earth
  Launch terrestrial precursors, convert to propellant on-orbit
  Lunar & Asteroid based ISRU
Propellant Types
  Cryogenic (LH2 / LO2)
  Hydrocarbon (e.g., CH4 / Kerosene)
  Hydrazine, etc.
Capability vs. Complexity
  Early: Propellant storage & transfer
  Mid: On-orbit electrolysis & chemical refining
  Later: ISRU
  Recommend progressive augmentation of capability

## Slide 20: Exploration benefits of refueling in LEO
Uses proven launch vehicle stages (existing assets + max heritage)
Increased payload to Moon / Mars
Lower cost orbital transfer (capital investment is not required for each maneuver)
Technology transfer to ISRU
Operational experience for ISRU
Defer HLLV investment ($10-20B)

## Slide 21: Civil applications of LEO refueling
Commercial & Science payload delivery (increases payload mass without requiring larger launch vehicle)
Remote sensing asset agility (more spacecraft fuel could extend ‘bandwidth’ of imaging opportunities)
Commercial & government space platforms (e.g, ISS, Bigelow)
Space Tourism (esp. Lunar)

## Slide 22: Defense Applications Exist
NRO (remote sensing) asset refueling
Large asset delivery (extending the ‘reach’ of launch vehicle fleet)
Robust applications across the DoD mission

## Slide 23: Applications to ISRU maturation
Lunar propellant manufacturing & utilization is a ‘big step’
  Convolution of several nested capabilities, including mining, extraction, separation, cryogenics, propellant transfer, etc.
  Common ISRU & fuel depot elements include power, cryo fluid handling, umbilicals, sensing & automation, as well as operations
A terrestrially-supplied LEO fuel depot could mature several key capabilities needed for ISRU
  Electrolysis, liquefaction & product storage
  Automated propellant transfer
  Vehicle checkout & certification
  Maintenance & repair
Note: A LEO fuel depot is a capability-building steeping stone, and will create the competency required to enable longer-term ISRU

## Slide 24: Features of the Water Rocket
a.k.a. the Centaur Tug
High-Gain Antenna
Payload
Adapter
Ring
Optional Manipulators
& Tool Rack
Water
Transfer
Port
LO2 Tank
LH2 Tanks
Solar Cell
Laminates
Water Tank
Zero-G Electrolysis Unit
GPS
Antenna
Extended Skirt

## Slide 25
sysRAND endeavors to leapfrog the rocket equation by solving the logistics equation
Thank You for your interest!