## Slide 1: COMPARATIVE STUDY OF ISRU-BASED TRANSPORTATION ARCHITECTURES FOR THE MOON AND MARS: LOX-LH2 vs. LOX-METHANE
Javier Díaz & Begoña Ruiz
Space Resources Roundtable VIII
Golden, Colorado
10-31-2006

## Slide 2: RESOURCE AVAILABILITY
Moon
Phobos
Mars
H2O | Ice Deposits | Poles | ~ 1.5% wt.
H2 | Solar Wind | Everywhere | ~ 50 ppm
C | Solar Wind | Everywhere | ~ 150 to 210 ppm
O2 | Pyroclastic Glass | Everywhere | ~ 4% (yield) wt.
CO2 | Atmosphere | Everywhere | ~ 95% wt.
H2O | Bound Water | Everywhere | ~ 10% wt.
H2O | Ice Deposits | Poles | Up to 90% wt.
O2 | Carbonaceous Chondrite | Everywhere | ~ 12.6% wt.
C | Carbonaceous Chondrite | Everywhere | ~ 4.43% wt.
H2O | Bound Water | Everywhere | ~ 10% wt.

## Slide 3: PERFORMANCE
LOX/H2
  Engines
    Isp: Up to 470 s
    Mixture ratio: ~ 6:1
    Reliable & Proven technology
  Storability
    LH2 Density: 0.07 g/ml
    Boiling point: 20.25 K
    Massive volume tanks
    Heavy tank insulation
LOX/CH4
  Engines
    Isp: Up to 370 s
    Mixture ratio: ~ 3.5:1
    Higher thrust (up to 50%) than eq. LOX/H2
    In development
  Storability
    LCH4 Density: 0.424 g/ml
    Boiling Point: 111.55 K

## Slide 4: PERFORMANCE
RD-0146 | LOX/H2 | LOX/CH4
Mass (kg) | 243 | 243
Thrust (kN) | 98 | 127
Isp (s) | 451 | 347
Mixture Ratio | 6 | 3.60
Engine: RD-0146 capable of multiple restarts

## Slide 5: 7 Missions Lunar Scenario
Establish a robotic propellant production capability for oxygen in an equatorial location
  Lunar tanker for Moon-L1-Moon is reusable
Deliver lunar oxygen to L1
Launch a dry Lunar Lander/Ascent Vehicle (LLAV) to L1
Fuel both the descent and ascent stages at L1 for the trip to and from the lunar surface back to L1
In the initial scenario, the LLAV is expendable (remains at L1)
  Subsequently, a reusable LLAV could improve scenario performance
The CEV is delivered to L1 separately, remains at L1 to the completion of the mission, then returns to Earth
In the initial scenario, the vehicles that deliver the LLAV and CEV to L1 are expendable
  Subsequently, a reusable OTV between LEO and L1 could be introduced
Human missions can go anywhere on the Moon
  They do not refuel on the Moon, so does not need to land at the propellant production facility
  Fueling is complete at L1. LLAV lands with full propellant for ascent
Robotic propellant production can be delivered with modest missions using expendable launch vehicles
Reusable propellant tanker provides feed-forward technology and operations to reusable human lander

## Slide 6: LUNAR LANDER
Assumptions
  Delta V lunar surface – EML1: 2778 m/s
  Lander Payload baseline: ESAS Lunar Mission (4 Crew)
  Mission duration: 20 days
  C concentration: 150 ppm (equatorial location)
  H2 concentration: 50 ppm (equatorial location)
  H2O concentration: 1% (polar location)
LOX/LH2 Lander
  Total Inert Mass: 9080 kg
  Required LH2: 4126 kg
  % LH2 boiloff during mission: 1.7 %
  Required LOX: 24754 kg
  % LOX boiloff during mission: 0.3 %
LOX/CH4 Lander
  Total Inert Mass: 6665 kg
  Required CH4: 8902 kg
  % CH4 boiloff during mission: 0.4 %
  Required LOX: 32047 kg
  % LOX boiloff during mission: 0.3 %

## Slide 7: LUNAR TANKER
LOX/LH2 Tanker
  Payload:
    LOX (for lander): 24754 kg
    LOX tank: 674 kg
    H2 (for lander): 4126 kg
    H2 tank: 1618 kg
  Total Inert Mass: 14284 kg
  Required LH2: 9226 kg
  % LH2 boiloff during mission: 1.2 %
  Required LOX: 55354 kg
  % LOX boiloff during mission: 0.2 %
LOX/CH4 Tander
  Payload:
    LOX (for lander): 32047 kg
    LOX tank: 856 kg
    CH4 (for lander): 8092 kg
    CH4 tank: 634 kg
  Total Inert Mass: 12224 kg
  Required CH4: 22671 kg
  % CH4 boiloff during mission: 0.2 %
  Required LOX: 78896 kg
  % LOX boiloff during mission: 0.2 %

## Slide 8: PROPELLANT & REGOLITH COMPARISON

## Slide 9: IMLEO COMPARISON

## Slide 10: Mars Ascent Vehicle
Assumptions
  Delta V mars surface – mars orbit: 4016 m/s
  Lander Payload baseline: 6269 kg (from DRM 3.0)
  Mission duration: 760 days
LOX/LH2 Lander
  Total Inert Mass: 9080 kg
  Required LH2: 4403 kg
  % LH2 boiloff during mission: 50.3 %
  Required LOX: 19611 kg
  % LOX boiloff during mission: 11.6 %
LOX/CH4 Lander
  Total Inert Mass: 6589 kg
  Required CH4: 5137 kg
  % CH4 boiloff during mission: 15.3 %
  Required LOX: 17997 kg
  % LOX boiloff during mission: 12.2 %
  H2 for Sabatier: 1481 kg
  Extra H2 tank: 626 kg

## Slide 11: FULLY REUSABLE ISRU MARS

## Slide 12: CONCLUSIONS
Assuming an lunar equatorial location, for a reusable lander between Moon and EML1, LOX/CH4 propulsion system option has lower mining and processing requirements than LOX/H2, being a better option if both oxidizer and fuel are produced on the Moon. This is assuming that H2 concentration (50 ppm assumed) is less than 60% C concentration (150 ppm assumed). If H2 concentration is 60% or higher than C concentration, LOX/H2 would be the best option
If only oxygen is produced on the Moon, LOX/LH2 would be a better option due to lower fuel requirements to be transported from Earth
Without the use of lunar polar resources (ice/hydrogen) the development of a reusable transportation architecture between EML1 and LEO supporting transportation to /from the Moon and Mars is not feasible
Production operations (water / hydrogen) in the polar regions maybe not feasible due to extreme environment conditions

## Slide 13: Questions?
Thank you!
jadiaz@mines.edu