## Slide 1: Lunar Electric Fields and Dust: Implications for ISRU
J.S. Halekas, G.T. Delory,
T.J. Stubbs, W.M. Farrell,
R.R. Vondrak, M.R. Collier

## Slide 2: The Pervasiveness of Lunar Dust
Makeshift fender on Apollo 17 lunar rover, necessitated by “rooster tails” of dust kicked up by rover motion on the surface.
Astronaut footprint in the dust at
the Apollo 11 landing site.
“Dust – I think probably one of the most aggravating, restricting facets of lunar surface
exploration is the dust and its adherence to everything no matter what kind…
and it’s restrictive friction-like action to everything it gets on… You have to live with
it but you’re continually fighting the dust problem both outside and inside the
spacecraft.” - Gene Cernan in his Technical Debrief.
Notes: Dust is everywhere on the surface

## Slide 3: Evidence for Dust Above the Lunar Surface
Unprocessed images of lunar horizon glow over western horizon just after sunset [Criswell, 1973; Rennilson and Criswell, 1974]
Horizon glow from forward scattered sunlight
Dust grains with radius of 5 – 6 μm at about 10 to 30 cm from the surface, where electrostatic and gravitational forces balance.
Horizon glow ~107 too bright to be explained by micro-meteoroid-generated ejecta [Zook et al., 1995].
Notes: Dust is levitated just above the lunar surface

## Slide 4: Dust Observed at High Altitude
Gene Cernan sketches
[McCoy and Criswell, 1974].
Schematic of situation consistent with Apollo 17 observations [McCoy, 1976].
Lunar dust at high altitudes (up to ~100 km).
0.1 μm-scale dust present sporadically (~minutes).
Notes: Dust is lofted to high altitudes.
The horizon glow in these sketches was also captured in photograph of the solar corona and zodiacal light (CZL) that were taken at the same time [see McCoy, 1976]. However, these sketches are useful since they capture details not caught by the coronal photography, as well as giving a sense of the time evolution of the phenomenon.

## Slide 5: In-Situ Evidence for Dust Transport
Terminators
Apollo 17 Lunar Ejecta and Meteorites (LEAM) experiment.
Berg et al., 1976
Notes: Dust transport is particularly prevalent near the terminators.
The LEAM experiment was placed on the Moon by Apollo 17 to detect hypervelocity impacts (~ 10 km/s) from interplanetary space.
However, surprisingly LEAM counts were dominated by slower moving (< 1 km/s) highly-charged dust grains which were almost certainly of lunar origin.
As shown in this plot, these counts peaked at the terminator, particularly at sunrise.
The greatest fluxes were seen in the east-west directions, which is consistent with the acceleration of charged dust grains in this region by a large horizontal E-field (due to transition from positive charging on the dayside to negative on the nightside – see next slide).

## Slide 6: The Lunar Electrodynamic Environment
Notes: Why is there so much dust flying around?
It’s the electric fields! Predicted in the 50s by Gold.
Moon exposed to solar wind plasma and energetic particles => surface charging.

## Slide 7: Occurrence of Extreme Lunar Charging
White = SEP Events
Grey = Magnetotail Passages
Halekas et al., 2006
Notes: Usually the charging is on the order of <100 V.
Really bad charging happens during SEP events and magnetotail crossings – correlated with high energy plasma and energetic particles.

## Slide 8: Charging During SEP Events
LP Magnetic Field
LP Electrons
ACE High Energy Protons
Lunar Surface Charging
Worst Charging Event Observed during Lunar Prospector (LP) mission.
Halekas et al., 2006
Notes: Here’s an example of extreme charging during an SEP event.
Charging likely caused by electrons, but this shows correspondence with SEP events.

## Slide 9: Dust Fountains
Energetic Particles
-
-
-
-
-
-
Negatively Charged Surface
Notes: Dust Sleet!
Dust is an important component of the lunar exosphere.
Dust, plasma, and neutral exosphere form a coupled system that we need to understand.

## Slide 10: Effects of Dust on Exploration/ISRU: Adhesion
Apollo 12 astronaut
Pete Conrad near
Surveyor 3. Note
finger mark in dust
layer on Surveyor 3
television mirror
NASA photograph AS12-48-7132
Dust on
EVA Suit
Dust was found to quickly and effectively coat all surfaces it came into contact with
during Apollo missions, including boots, gloves, suit legs and hand tools - this
resulted in clogging of mechanisms, abrasion, thermal control problems and
seal failures [Gaier, 2005].
Adhesion efficiency is likely increased by the angular barbed shapes of lunar dust,
and possibly also by electrostatic charging.
Notes: What’s all the dust going to do for exploration and/or ISRU.
First of all, it sticks to everything.

## Slide 11: Effects of Dust on Exploration / ISRU: Abrasion and Clogging
Pete Conrad noted that EVA suits were more worn after 8 hrs of surface activity than training suits were after 100 hr, and that suits were worn through the outer layer and into the Mylar insulation above the boot.
Gauge dials were so scratched up during Apollo 16 as to be unreadable, and Harrison Schmitt’s sun shade on his face plate was so scratched that he could not see in certain directions.
There were reports of clogging and jammed mechanisms on every Apollo mission, including equipment conveyors, lock buttons, camera equipment, Velcro fasteners, suit mechanisms, and even the vacuum cleaner designed to clean off the dust.
Gaier, 2005.
Notes: It abrades material and clogs mechanisms.

## Slide 12: Effects of Dust on Exploration/ISRU: Toxicity
SEM images of A17 dust 70051 [Park et al., 2006]
Lunar dust is extremely angular
(barbed), increasing inhalation
hazards and eye and lung
irritation.
Dust may also have reactive
volatiles on its surface
(Apollo crews reported a “gun
powder” smell).
Notes: It’s nasty to breathe.

## Slide 13: Effects of Electric Fields on Exploration/ISRU
Spacecraft charging and electrostatic
discharge (ESD) have caused by far
the most environmentally related
anomalies on spacecraft, and surface
charging has caused the most serious
anomalies, i.e. those resulting in mission
loss [Koons et al., 2000; Bedingfield et al.,
1996; Leach and Alexander, 1997].
On the surface of the Moon, machinery
is exposed to the same plasma charging
currents, plus electric fields and dust
associated with surface effects.
Electrostatic Discharge
Notes: Electric fields may have plenty of serious effects all by themselves.

## Slide 14: Some Needed Measurements
Measurement | Instrumentation
Exospheric dust concentrations | Photometer (passive) LIDAR (active)
Dust transport properties (mass, velocity and charge distributions) | Impact sensor (more sensitive and discriminating than LEAM)
Surface electric fields | E-fields instrument with boom (and maybe magnetometer)
Plasma characteristics | Electron spectrometers Ion spectrometers
Both orbital and surface-based measurements needed.

## Slide 15: Conclusions
The lunar environment is complex, with dust, plasma and electric fields, and the neutral exosphere all tightly coupled.
Dust and electric fields may have a significant effect on exploration/ISRU efforts.
Targeted measurements are necessary in order to understand the dusty electrodynamic lunar environment.