## Slide 1
D Rickman, C Owens, R Howard, C McLemore
Marshall Space Flight Center
Nov 2, 2006
REQUIREMENTS AND TECHNOLOGIES FOR
DEVELOPING AND MEASURING SIMULANT
SPACE RESOURCES ROUNDTABLE VIII

## Slide 2: Contributors
Susan Batiste University of Colorado, Boulder
Paul Carpenter BAE Systems Analytical and Ordnance Solutions
Raymond French MSFC/NASA
Hans Hoelzer Teledyne Brown Engineering
Rick Howard Teledyne Brown Engineering
Chuck Owens Teledyne Brown Engineering
John Lindsay Lunar and Planetary Institute
Carole McLemore MSFC/NASA
Sarah Noble JSC/NASA
Doug Stoeser USGS
Doug Rickman MSFC/NASA
Ian Ridley USGS
Laurent Sibille ASRC Aerospace Corp
Susan Wentworth ERC, Inc., Engineering and Science Contract Group
Steve Wilson USGS

## Slide 3: A Description of Lunar Regolith
Lunar Sourcebook, 1991
Notes: Some questions are remarkably basic and are more or less commonly recognized.

## Slide 4: Requirements
There are requirements for the project.
The overall effort must be practical. This is an engineering effort.
The simulant should have known characteristics.
The user should understand the simulants limitations.
It must be practical to compare results from different simulants.
Simulant must be suitable for a wide range of needs.
There are requirements for the simulant.
Duplicate what will be found on the Moon to a sufficient degree and to the extent practical.

## Slide 5: Intended Users
Manufactures
Users
  Procurement
  Limitations
  Storage
  Use
  Reuse
Project Management

## Slide 6: Basic Facts about Regolith
Sample heterogeneity is higher than anything terrestrial.
Lithology and mineralogy range across the igneous spectrum but are dominated by a small subset.
Some of the compositions of interest are at the limits or outside the bounds of terrestrial samples.
Lithic fragments, glass, minerals and agglutinates are the major constituents
Many minor phases (less than 5% but greater than 1000 ppm) exist and are wide spread. Some of these phases are likely to be major problems for extractive processes. Examples include S, P, Cl, and F.
Agglutinates are locally very abundant, forming the majority of the regolith.

## Slide 7: What We Don’t Know
It is impossible at this time to know how much simulant to make.
We don’t know all the users of the simulant.
We don’t know where we are landing on the Moon.
Even if we knew where we were landing, unless it is one of the Apollo sites, we don’t know its geology (selenology).

## Slide 8: Technical Specialties
What is on Earth and how to put the simulant together
Economic Geology
Mining
Extractive metallurgy (grinding, etc.)
Particle size measurement
Mixing of particulate material
What actually exists on the Moon
Lunar geology (selenology)

## Slide 9: Approach
Multiple tasks done in parallel - many tasks are iterative
Acquire the necessary characterization of the lunar samples
Establish process control technology through a prototype effort
Identify suitable source materials
Develop the FoM algorithm
Define terminology, methodology, baseline conditions and provide users with guidance
Provide FoM for all available simulants
Demonstrate the practicality and cost performance of production

## Slide 10: Figures of Merit
Four characteristics
  Composition
    Lithic Fragments
    Mineralogy
    Glass
    Agglutinate
  Size Distribution
  Shape (may subdivide this)
  Density
Measurement methods are stipulated
Compare simulant to specific Apollo regolith samples (core and/or surface samples)

## Slide 11: Figures of Merit, Commentary
  Expressed as a computer algorithm with fixed inputs.
  Designed to be extensible in response to new knowledge or needs
  Many, many practical virtues
    Can compare between simulants
    Standardized, objective method
    Users do not have to understand the all the details of the background skills which go into making the simulant
    Producers shielded from vague specifications