## Slide 1: ISRU-BASED TRANSPORTATION ARCHITECTURES FOR THE MOON USING DIRECT 2.0 LAUNCH VEHICLES
Javier Diaz & David Vivanco
Space Resources Roundtable IX
10/25/2005
Golden, Colorado

## Slide 2: Direct 2.0
Proposal to replace Ares I & Ares V launch vehicles with a single “universal launcher”
First member of the family consists entirely of existing flight articles in active service today
Additional members incorporate new upper stage to be powered by the J-2XD engine, of Saturn heritage
Authors: Stephen L Metschan, Cyril A Longton, Ross B Tierney, António H F Maia, Philip J Metschan, Chuck Longton, study produced by nearly 50 NASA engineers.
http://www.directlauncher.com/

## Slide 3: Direct 2.0

## Slide 4: Direct 2.0

## Slide 5: Launch System: Ares I&V vs. Jupiter
Ares I&V: based on two different launchers
  Ares I: 25mt to LEO, man rated
  Ares V: 130mt to LEO
Jupiter: a single launcher in two configurations able to launch crew and cargo with a performance of up to 108t in LEO
  Jupiter 120: 45mt to LEO
  Jupiter 232: 108mt to LEO

## Slide 6: Launch System: Ares I&V vs. Jupiter
Capabilities:
  A Jupiter 120 is more performing than an Ares I, allowing for growth margins of the CEV and more architecture flexibility.
  A Jupiter 232 is less performing than an Ares V, however the proposed exploration architecture does not require such big performances.

## Slide 7: Launch System: Ares I&V vs. Jupiter
Development cost: the higher communalities of the Jupiter system with the Shuttle existing hardware and between the two configurations make it cheaper to develop (∆= -10B$ with respect to Ares I&V)
Operating cost: the Jupiter system presents lower recurrent costs (∆= -1.5B$/yr with respect to Ares I&V) due to:
  a sole launch system is used, reducing operations
  the higher launch rate of the system allows to have lower unitary costs

## Slide 8: Cost Comparison: Ares I&V vs. Jupiter

## Slide 9: Lunar ISRU Architecture Description
Establish a robotic propellant production capability for oxygen and hydrogen in a polar location
Deliver lunar oxygen and hydrogen to EML1
Utilization of reusable/refuelable landers:
  Lunar Tanker for Moon-L1-Moon is single stage & reusable. Lifetime: 8-16 Missions
  Lunar Crew Lander for Moon-L1-Moon is single stage & reusable. Lifetime: 4-8 Missions
Predeployment of ISRU propellant production plant and Lunar Tanker
Launch a dry Lunar Crew Lander to EML1
Fuel the Lunar Crew Lander at L1 for the trip to and from the lunar surface back to L1
The Lunar Crew Lander remains at L1 after the mission is completed
The CEV is delivered to L1 separately, remains at L1 to the completion of the mission, then returns to Earth
In the initial scenario, the EDS that deliver the landers and CEV to EML1 are expendable
  Potential for reuse expended EDS to build a EML1 fuel depot
  Subsequently, a reusable EDS between LEO and L1 could be introduced
Human missions can go anywhere on the Moon
  They do not refuel on the Moon, so does not need to land at the propellant production facility
  Fueling is complete at L1. Lunar Crew Lander lands with full propellant for ascent

## Slide 10: Lunar ISRU Architecture
EML1
LEO
ISRU Plant
EDS
Lunar Tanker
EDS
Expended
Lunar Crew Lander
EDS
ISRU Plant
Refueling with lunar propellant
EDS
Expended
Docking + refueling
Docking + Crew Transfer
Lunar Crew Lander remains at EML1 for reuse
Lifetime 4-8 missions
EDS
Expended
ORION
EDS
Docking + Crew Transfer
Lunar Tanker Lifetime 8-16 missions
Opportunity for future collection of expended EADS to start building a EML1 Fuel Depot
Service Module Expended
Crew Module Land Landing

## Slide 11: IMLEO comparison

## Slide 12: ESAS LSAM
Ascent Stage
  Total Inert Mass: 6276 kg
  Required propellant: 6238 kg
  NTO/MMH Propulsion
Descent Stage
  Total Inert Mass: 11049 kg
  Required propellant: 30319 kg
  LOX/H2 Descent Propulsion
  4 Modified RL10
  Payload (Cargo)
    21000 kg to Lunar Surface

## Slide 13: Lunar ISRU Vehicles
Lunar Crew Lander
  Single Stage
  Reusable
    Lifetime 4-8 missions
  LOX/H2 Propulsion
  3 Modified RL10
  Lander Payload baseline: ESAS Lunar Mission (4 Crew)
  Total Inert Mass: 9974 kg
  Required LH2: 3977 kg
  Required LOX: 23863 kg
  Delta V lunar surface – EML1: 2778 m/s
Lunar Tanker / Transporter
  Single Stage
  Reusable
    Lifetime 8-16 missions
  LOX/H2 Propulsion
  6 Modified RL10
  Payload (Tanker):
    LOX (for lander): 23863 kg
    LOX tank: 714 kg
    H2 (for lander): 3977 kg
    H2 tank: 1870 kg
  Payload (Transporter)
    15750 kg from EML1 to Lunar Surface
  Total Inert Mass: 14599 kg
  Required LH2: 9226 kg
  Required LOX: 55354 kg

## Slide 14: ISRU Propellant Plant
Assumptions
  Average content predicted to be 1.5% by Lunar Prospector (LP) neutron spectrometer data (Feldman et al, 2001)
  Thought to be located within craters larger than 10 km
  Form is uncertain, may range from ice lenses to ice coatings on regolith grains to granular mixtures of ice and dirt particles; physical properties unknown
  LP data suggest deposits may be covered by 40 cm of dry regolith
  Range of concentration may exist – up to 10% by weight

## Slide 15: ISRU Propellant Plant
Assumptions
  Ice is uniformly mixed with regolith at concentrations of 1.5%
  Mechanical properties of icy regolith are similar to those of regolith elsewhere on Moon (fine-grained, granular, highly compacted, but mechanically weak)
  Temperature of surface ~ 80K
  Ice can be extracted by raising temperature by 150K in a closed reactor
  Location: Shackelton Crater
  Several areas with greater than 80% sunlight and less extreme temperatures (assumed 70%)

## Slide 16: ISRU Propellant Plant
Plant Mass: 9121 kg
Power requirement: 440 kW, provided by solar panels
Production Rate:
  Oxygen: 201.35 mt/yr
  Hydrogen: 25.17 mt/yr
10% / yr mass requirement for refurbishment

## Slide 17: Lunar Architectures Cost Analysis: ESAS vs. ISRU
Assumptions:
  FY05 $
  2019-2025
    2 Crew missions/yr
    1 Cargo mission/yr
  Lifetime for reusable landers:
    4 Missions for Lunar Crew Lander
    12 Missions for Lunar Tanker
Results:
  Reusable Landers + ISRU Plants development costs 22% higher than ESAS system
  Reusable Landers + ISRU Plants production cost (unit total system) 53% higher than ESAS system

## Slide 18: Cost Structure Analysis

## Slide 19: Conclusions
Direct 2.0 Jupiter uses only one launcher with different configurations, capable of performing both Ares I and Ares V roles. By sharing and reusing many Shuttle components with minimal alterations, developing costs, operation costs and schedule reductions will be accomplished.
These reductions may bring the opportunity of early ISRU integration for lunar missions within original VSE cost structure.

## Slide 20: Conclusions
The described ISRU based Lunar Architecture will maximize this savings and improve performance over ESAS baseline architecture by:
  Reducing the mass to be launched per mission
  Reducing the required size and number of launch vehicles
  The use of EML1 vs. LLO and a reusable on orbit fueled Crew Lander at EML1 allows to:
    Full access to the moon, not being constrained to a single lunar outpost
    Continuous return window from any point of the lunar surface
    Lower in space transit time between the Earth and Moon
    Daily departure window from the Earth
    Potential for expandability. By increasing propellant production capacity on the Moon, and creation of a propellant tank in EML1, a ISRU based reusable transportation architecture between EML1 and LEO could be develop in order to support transportation to/from the Moon and Mars

## Slide 21: Conclusions
Identified Key technologies:
  Autonomous operations
    Rendezvous and Docking
    Payload transfer
    Propellant tank transfer
    Propellant tank tapping
    Lunar landing
    Payload offload
    Lunar Transportation SystemsTM
  One stage lander design
    Lockheed Martin
  Low boil-off rate for cryogenic storage
    Active cooling: Lockheed Martin COLD technologies. 0.01% per day
    Passive cooling: ICES (Integrated Cryogenic Evolved Stage). 0.1% per day

## Slide 22: Thank you!
Questions?
Javier Díaz javdiaz@gmail.com
David Vivanco vivanco.d@gmail.com