## Slide 1
WHY GU9?
Sun centered orbit
  GU9 orbits the sun at approximately the same distance as does Earth
Orbit similar to that of Earth
  While at a higher inclination and a longer eccentricity, GU9’s orbit closely resembles that of Earth
  GU9’s location is always within a few degrees of the Earth/Sun Radial
Frequency of potential launch and return dates
  Because of these similarities, GU9 serves as a target that has frequent opportunities for visitation
  Always visible from earth,
  easing communications requirements
Image Credit: NASA JPL

## Slide 2
The Orbits
Corkscrew effect
  Due to the similar orbits about the Sun, GU9’s orbit relative to earth is like a corkscrew
There are key locations in the orbit (the ascending and descending nodes) where:
  The relative velocity between the Earth and GU9 is at a minimum
  The range is at a minimum
Image Credit: NASA JPL
Note two times per orbit when GU9’s orbit crosses Earth’s orbital plane
2004 GU9’s relative range and velocity to Earth over a 5 year period

## Slide 3
The Mission
Depart from earth orbit (300 km)
  For the purposes of these simulations, it is assumed that the spacecraft is already in a parking orbit around the Earth
    Earth to parking orbit launches are not considered
    It is assumed that the parking orbit is aligned as necessary ahead of time, as required to perform the desired interplanetary maneuvers (inclination and phasing)
Arrive at asteroid safely
  In all cases, it is assumed that the spacecraft is meant to arrive at GU9 with no relative velocity
    This does not account for a ‘soft’ landing on the surface of the asteroid nor does it determine the necessary velocities needed for maneuvering or to orbit the asteroid as there is insufficient data available to perform such calculations

## Slide 4
Flight Option 1
This method uses two orbital maneuvers. First, a Hohmann transfer is performed to match the non-inclined orbit of the asteroid. Secondly, a plane change is performed to match the orbits
Pros
  This is a relatively ‘quick’ transfer at around 275 days (see following slides)
  The Hohmann transfer is highly fuel efficient and burning in the direction of Earth’s orbit will save even more fuel
Cons
  The inclination change and following slow-down maneuvers are very expensive in terms of fuel (at the expense of useable payload capacity)
  Decreased useful payload due to higher fuel requirements

## Slide 5
1. Burn from Earth orbit
2. Hohmann transfer to GU9 ‘flat’ orbit
3. Inclination plane change
4. Slow-down burn at GU9
Earth’s position at time of launch (counter-clockwise orbit)
GU9’s position at time of launch (counter-clockwise orbit)
The probe’s Hohmann transfer trajectory (counter-clockwise orbit)
The probe’s intercept with the ascending node of GU9’s path and burn to change its inclination
Arrival at GU9 and resulting slow down burn
Maneuver diagram - Flight Option 1
1.
2.
3.
4.

## Slide 6
1. Burn from Earth orbit accelerates the spacecraft along the same direction as the motion of the Earth about the Sun
2. Hohmann transfer (from burn in step 1) is performed. The higher velocity of the spacecraft shortens its orbital period, allowing it to reach 2004 GU9 on the other side of the solar system before Earth would normally arrive.

## Slide 7
3. Upon arriving at 2004 GU9’s ascending node, a burn is performed to change the inclination of the spacecraft
4. Upon arriving at 2004 GU9’ a burn is performed to slow the spacecraft to match the asteroid’s velocity

## Slide 8
Earth departure
Hohmann transfer
Burn to change inclination
Arrival slow-down
Earth departure
Hohmann transfer
Arrival
The spacecraft’s range from GU9 during the course of the maneuvers
The spacecraft’s relative velocity to GU9 during the course of the maneuvers

## Slide 9
Viable Launch Dates
Dates that a departure could take place
Launch |  | Arrival |  | Travel Time (days)
Date | Time ± 1 hour | Date | Time ± 2 hours | 
2/21/08 | 3:30 PM | 11/20/08 | 4:29 PM | 273.0415
2/21/09 | 6:30 AM | 11/21/09 | 9:59 AM | 273.1457
2/21/10 | 9:00 PM | 11/22/10 | 2:59 AM | 273.2498
2/22/11 | 12:00 PM | 11/22/11 | 8:29 PM | 273.354
2/23/12 | 2:30 AM | 11/22/12 | 1:29 PM | 273.4582
2/22/13 | 5:30 PM | 11/23/13 | 6:59 AM | 273.5623
2/23/14 | 8:00 AM | 11/23/14 | 11:59 PM | 273.6665
2/23/15 | 11:00 PM | 11/24/15 | 5:29 PM | 273.7707
2/24/16 | 1:30 PM | 11/24/16 | 10:29 AM | 273.8748
2/24/17 | 4:30 AM | 11/25/17 | 3:59 AM | 273.979
2/24/18 | 7:00 PM | 11/25/18 | 8:59 PM | 274.0832
2/25/19 | 10:00 AM | 11/26/19 | 2:29 PM | 274.1873
2/26/20 | 12:30 AM | 11/26/20 | 7:29 AM | 274.2915
2/25/21 | 3:30 PM | 11/27/21 | 12:59 AM | 274.3957
2/26/22 | 6:00 AM | 11/27/22 | 5:59 PM | 274.4998
2/26/23 | 9:00 PM | 11/28/23 | 11:29 AM | 274.604
2/27/24 | 11:30 AM | 11/28/24 | 4:29 AM | 274.7082
2/27/25 | 2:30 AM | 11/28/25 | 9:59 PM | 274.8123
2/27/26 | 5:30 PM | 11/29/26 | 3:29 PM | 274.9165
2/28/27 | 8:00 AM | 11/30/27 | 7:59 AM | 274.9998
2/28/28 | 11:00 PM | 11/30/28 | 1:29 AM | 275.104
2/28/29 | 1:30 PM | 11/30/29 | 5:59 PM | 275.1873
3/1/30 | 4:30 AM | 12/1/30 | 11:29 AM | 275.2915
3/1/31 | 7:00 PM | 12/2/31 | 3:59 AM | 275.3748
3/1/32 | 10:00 AM | 12/1/32 | 9:29 PM | 275.479
3/2/33 | 12:30 AM | 12/2/33 | 1:59 PM | 275.5623
3/2/34 | 3:30 PM | 12/3/34 | 7:29 AM | 275.6665
3/3/35 | 6:00 AM | 12/3/35 | 11:59 PM | 275.7498
3/2/36 | 9:00 PM | 12/3/36 | 5:29 PM | 275.854
3/3/37 | 11:30 AM | 12/4/37 | 10:29 AM | 275.9582

## Slide 10
Flight Option 2
This method also uses two orbital maneuvers and requires very precise timing. First, when Earth’s orbit crosses the ascending or descending node of the asteroid, a burn is performed to inject the probe/spacecraft directly into the orbital plane of GU9. Secondly, a phase change maneuver is performed to help the spacecraft ‘catch-up’ with the asteroid.
Pros
  The lack of a plane change maneuver saves significant amounts of fuel
  Increased useful payload because of fuel savings
Cons
  This is a slower transfer at around 360+ days (see following slides)
    May have implications on manned missions
  The full momentum from Earth’s rotation about the sun can’t be utilized to its maximum potential

## Slide 11
Maneuver diagram - Flight Option 2
Earth’s position at GU9 arrival (counter-clockwise orbit, 1 year later)
Earth’s position at time of direct-inject burn
Phase change maneuver to catch up to the asteroid
Burn from inclined Earth orbit
Direct insertion into GU9 heliocentric orbit
Phase correction to adjust for intercept
GU9 arrival (counter-clockwise orbit, 1 year later)
1, 2
3.

## Slide 12
1-2. When Earth crosses the ascending node of the asteroid, the spacecraft is launched from an inclined orbit (matching the relative inclination of the asteroid) directly into the orbital plane of 2004 GU9

## Slide 13
3. While in the orbital plane of 2004 GU9, the spacecraft will be behind the asteroid in its orbit. In order to catch up, a phase change maneuver is performed to move the spacecraft to the same point in the orbit as the asteroid.
The phase change orbit is a smaller elliptical orbit that has a faster period than that of the target. When the spacecraft is behind the asteroid, this faster orbit will get it around the sun and back to the same point as where it left within (ideally) the exact amount of time it takes the target (the asteroid) to finish its orbit and get to that same point. As they are on the same orbit, the phase change maneuver is all that is required to match orbital speeds with the target.

## Slide 14
Earth departure
Arrival slow-down
Earth Departure: Matched inclination burn from Earth orbit
Phase change maneuver to ‘catch up’
Phase change maneuver to ‘catch up’
The spacecraft’s range from GU9 during the course of the maneuvers
The spacecraft’s relative velocity to GU9 during the course of the maneuvers

## Slide 15
Launch |  | Arrival |  | Travel Time (days)
Date | Time ± 1 hour | Date | Time ± 2 hours | 
4/30/07 | 5:30 PM | 4/24/08 | 2:29 AM | 359.374611
4/29/08 | 11:30 PM | 4/24/09 | 4:38 PM | 359.714051
4/30/09 | 6:00 AM | 4/25/10 | 7:16 AM | 360.053437
4/30/10 | 12:30 PM | 4/25/11 | 9:54 PM | 360.392258
4/30/11 | 7:00 PM | 4/25/12 | 12:31 PM | 360.730514
4/30/12 | 1:30 AM | 4/26/13 | 3:08 AM | 361.068211
4/30/13 | 7:30 AM | 4/26/14 | 5:12 PM | 361.404629
4/30/14 | 2:00 PM | 4/27/15 | 7:47 AM | 361.741182
4/30/15 | 8:30 PM | 4/26/16 | 10:21 PM | 362.077183
4/30/16 | 3:00 AM | 4/27/17 | 12:54 PM | 362.412638
4/30/17 | 9:00 AM | 4/28/18 | 2:55 AM | 362.746690
4/30/18 | 3:30 PM | 4/28/19 | 5:26 PM | 363.081026
4/30/19 | 10:00 PM | 4/28/20 | 7:57 AM | 363.414822
4/30/20 | 4:30 AM | 4/28/21 | 10:27 PM | 363.748084
4/30/21 | 10:30 AM | 4/29/22 | 12:24 PM | 364.079824
4/30/22 | 5:00 PM | 4/30/23 | 2:53 AM | 364.411992
4/30/23 | 11:30 PM | 4/29/24 | 5:20 PM | 364.743634
4/30/24 | 6:00 AM | 4/30/25 | 7:47 AM | 365.074753
4/30/25 | 12:00 PM | 4/30/26 | 9:42 PM | 365.404235
4/30/26 | 6:30 PM | 5/1/27 | 12:07 PM | 365.734286
5/1/27 | 1:00 AM | 5/1/28 | 2:31 AM | 366.063823
4/30/28 | 7:30 AM | 5/1/29 | 4:55 PM | 366.392849
4/30/29 | 1:30 PM | 5/2/30 | 6:46 AM | 366.720125
4/30/30 | 8:00 PM | 5/2/31 | 9:09 PM | 367.048109
5/1/31 | 2:30 AM | 5/2/32 | 11:30 AM | 367.375591
4/30/32 | 9:00 AM | 5/3/33 | 1:51 AM | 367.702575
4/30/33 | 3:30 PM | 5/3/34 | 4:11 PM | 368.029063
4/30/34 | 9:30 PM | 5/4/35 | 5:59 AM | 368.353663
5/1/35 | 4:00 AM | 5/3/36 | 8:17 PM | 368.679139
4/30/36 | 10:30 AM | 5/4/37 | 10:35 AM | 369.004130
Viable Launch Dates
Dates that a departure could take place

## Slide 16
Required fuel
Amount of fuel required to achieve necessary velocities

## Slide 17
Digital Space Concept Videos

## Slide 18
Digital Space Concept Videos

## Slide 19
Digital Space Concept Videos

## Slide 20
Digital Space Concept Videos